## Slide 1
CUY-17/94/480-10.78/10.05/13.04
Safety Funding Application ODOT District 12
Brookpark

## Slide 2: Introductions
Brian Blayney, ODOT District 12
Kevin Miller, LJB
Scott Knebel, CMT

## Slide 3: Purpose and Need
Increase capacity of the critical intersection (Brookpark Road)
Reduce queues on the WB exit ramp that extend onto mainline I-480 and through adjacent intersections on State Road
Improve lane continuity to reduce unnecessary lane changes

## Slide 4: Area Map
Recurring congestion
during PM peak hour
1.6 miles
SR 94
I-480
SR 176
750’
SR 17 (Brookpark Rd)
EB Exit 
Urban Int Rank:
-2010 – 35
-2012 – 99
-2013 – 87
Urban Fwy Rank:
-2010 – 83
-2012 – 64
-2013 – 67
 WB Exit
I-480
SR 94 (State Rd)
350’
Notes: Closely spaced intersections on State Road from I-480 ramps to Brookpark Road intersection
Safety Analyst Ranking:
I-480 – Year 2012 (64), Year 2013 (67)
SR 94 and Brookpark intersection – Year 2010 (35), Year 2013 (87)

## Slide 5
Existing Conditions, PM Peak
(1) At I-480 WB Exit Looking East (2) At EB Exit Looking South (3) At Brookpark Looking North
1
2
EB Exit Ramp Blocked by SR 94 SB Queues from Brookpark
3
I-480 WB Exit Ramp Queue Spillback
SR 94 SB Queues at Brookpark Extending to EB Ramp Intersection
Notes: Queues extend from the Brookpark intersection during AM and PM peak periods
Closely spaced ramp intersections cannot provide sufficient storage for turning movements to/from I-480
Queues on I-480 WB exit ramp to State Road extend to mainline I-480 during PM peak

## Slide 6
Unmet demand, NB inner through lane at the end of green
Residual queue at the end of green
Existing Conditions
1
2

## Slide 7: Crash Summary
location | TOTAL | REAR END (30.9%) | ANGLE / LT (20.8%) | FIXED OBJECT (14.6%) | SIDESWIPE PASSING (8.7%) | TOD (6-9AM) | TOD (3-6PM) | ODOT RSI
SR 94/ Brookpark | 76 | 42 (55.3%) | 18 (23.7%) | 5 (6.6%) | 6 (7.9%) | 19.7% | 32.9% | 22,820
SR94/I-480 EB Ramps | 43 | 24 (55.8%) | 9 (20.9%) | 2 (4.7%) | 7 (16.3%) | 18.6% | 18.6% | 20,795
SR94/IR-480 WB Ramps | 36 | 19 (52.8%) | 11 (30.6%) |  | 6 (16.6%) | 8.3% | 27.8% | 22,356
201 total crashes (2011-2013)
  61 injury accidents (30% vs 25% average)
  99 rear end crashes (49% vs 31% average)
  48% of crashes occur during AM and PM peaks
Notes: 189 crashes on State Road and its intersections from Brookpark to Ralph/Burger
An additional 12 crashes on I-480 WB mainline near the State Road exit ramp/gore area during weekday PM peak hour conditions

## Slide 8: Countermeasures
Add WB right turn lane on Brookpark Road at State Road (350’)
Extend storage lengths on the I-480 WB Exit ramp (600’) (L-L-R)
Revise interchange phasing to operate Buckeye diamond sequence
Revise lane configuration on NB approach at the I-480 EB ramp from T(L)-T-TR-R configuration to a T(L)-T(L)-T-R configuration
Notes: Adding WB right turn lane increases intersection capacity
WB exit turn lane extension mitigates ramp queues/crashes
NB lane mitigates lane imbalance
  70% of approach volumes destine to WB ramp
  Only single right turn onto EB entrance ramp is possible
  Lane-use sign upgrades

## Slide 9: Countermeasures
Revise lane configuration on SB approach at the I-480 WB ramp from T-T-TR configuration to a T(L)-T-T-R configuration
Restripe auxiliary turn lanes on State Road at Wetzel/ Springdale
**No pavement widening needed on State Road!
Notes: 5) Channelize SB inside lane mitigates left turn crashes at WB ramp intersection
Improvements on State Road assume overlay on existing pavement without widening.

## Slide 10: Proposed Improvements SR 94 (State Road)
N
Notes: Add a WB right turn lane at Brookpark/State Rd intersection (Additional ROW required)
(-) Restripe NB receiving lanes on State Road from the Brookpark intersection from 3 lanes to a 2-lane section for better channelization.
(3) Revise NB approach at EB ramps intersection from the existing T(L)-T-TR-R configuration to a T(L)-T(L)-T-R configuration. The T(L) lane designation represents the back of the NB-to-WB left turn slots, south of the EB exit ramp intersection. Expand throat width on inside of NB double left to I-480 WB.
(5) Revise the SB approach at the WB ramps intersection from the existing T-T-TR to a T(L)-T-T-R configuration. The T(L) lane designation represents the back of the SB-to-EB left turn slot, north of the WB exit ramp intersection.
(6) Form left turn lanes on State Road between WB ramps and Ralph/Burger Avenue within existing pavement width.
NOTE: Improvements on State Road can be accommodated within existing pavement.

## Slide 11: Proposed Improvement Plan I-480 WB ramp
SR 94
WB Ramp
I-480
N
600’
Notes: Widen WB exit ramp turn lanes from 200’ to 600’

## Slide 12: Program Management
Minor signal upgrades to improve turn lane detection and signal head visibility installed 2014
Targeted improvements to reduce queuing on WB exit
Long-term need for dual SB left turn lanes deferred; too costly, produces diminishing returns

## Slide 13: Funding Summary
$97,400 safety study completed
$350,000 for Environmental/PE and Detailed design
$133,000 Right of Way
$2.26M Construction Cost
  30% design risk
  8.5% inflation cost
$2.83M Total Safety Funding Request
Notes: Interchange Operations Study (IOS) Required

## Slide 14: Scoring
Benefit cost ratio = 1.23
Existing volume to capacity ratio >1.0 with demand volumes factored into analyses
Percent PSI to Total Expected Crashes = 8%
Annual Crash reduction = 5.7 crashes

## Slide 15: Summary
Safety Project
  Mitigates safety hot spot (#35 in 2010)
  Reduces queues on WB exit and through adjacent intersections on State Rd
  Reduces weaving in congested corridor
RW impacts minimized at Brookpark Road