203		20000 	EMBANKMENT

Avg.Width x [Ht of Embankment] x  Wall Avg width under of 1358A

10’ x 21’x 112’

23520 cf

Quantity:  871 CY

___________________________________________________________________

203		35110 	GRANULAR MATERIAL, TYPE B

2073 (SF) [Cad  Area from behind footing.] x (13.8)Ht avg of Material

Quantity:  1060 CY

_____________________________________________________________________

203		35120 	GRANULAR MATERIAL, TYPE C

(CAD measured under SGF and area infront of wall) x 1.0’ (Thickness)

3992x1

Quantity:  148 CY

______________________________________________________________________

512               10100	SEALING OF CONCRETE SURFACES (EPOXY-URETHANE)

2515 [SF] (Exposed wall face, CAD measured)

+ 141 [FT] (measured along bottom of coping) x 4.5/12 [FT]

+ 141 [FT] (measured along top of coping 10/12 [FT] = 4726.4 [SF]

= 2515+141 [SY]

Quantity: 295 SY

____________________________________________________________________

516                13200	1/2” PREFORMED EXPANSION JOINT FILLER

141 [FT] (measured along top of coping) / 20 [FT/JOINT] = 8 JOINTS

= 8 [JOINTS] x 1.31 [SF/JOINT](Coping Joint section area, measured in cad) = 10.48 [SF]

Quantity:  11 SF

______________________________________________________

516	13900		2” PREFORMED EXPANSION JOINT FILLER

87 [FT] (measured along top of wall in front of abutment) x 0.5 [FT]

x 2sides = 179 [SF]

Quantity:  87 SF

530                13000	FORM LINER

3150 [SF] (CAD measured)

Quantity:  3150 SF

____________________________________________________________________

840                20000	MECHANICALLY STABILIZED EARTH WALL

3150 [SF] (CAD measured)

Quantity:  3150 SF

____________________________________________________________________

840                 21000         WALL EXCAVATION

(Cad Area SGB limits + 2ft limits) x Avg Thickness of Ext Ground

4089 x 5.5ft

Quantity: 833 CY

__________________________________________________________________

840               22000            FOUNDATION PREPARATION

(Cad Area SGB limits + 2ft limits)

4089 SF

Quantity:  454 SY

____________________________________________________________________

840		23000		SELECT GRANULAR BACKFILL

(Cad Area SGB limits) x Avg. Thickness of Material

3674SF x 24.5FT

= 90,013 CF

Quantity: 3334 CY

840	25010		6” DRAINAGE PIPE, PERFORATED

132 +10 + 142.0 [FT] = 284 [FT]

Quantity:  284 FT

840	25020		6” DRAINAGE PIPE, NON-PERFORATED,

43.7 [FT] = 44 [FT]

Quantity:  44 FT

840                 26000            CONCRETE COPING

141 [FT] (measured along top of coping) = 141 [FT]

Quantity:  141 [FT]

840		26050	             AESTHETIC SURFACE TREATMENT

2515 [SF] (CAD measured)

Quantity: 2515 SF

______________________________________________________________________

840		27000		ON-SITE ASSISTANCE

1 DAY

Quantity: 1 DAY

______________________________________________________________________

840		23050		NATURAL SOIL

(Cad Area SGB limits) x Avg Thickness of Ext Ground

(828 SF + 607 SF) x 2ft / 27 = 106.3 CY

Quantity: 107 CY