Ohio Department of Natural Resources Application

To Obtain a Corridor License Agreement

Submission of Proposal:

All submissions to obtain a corridor license agreement shall contain the following:

- Proposed route maps and survey data.  These maps should be produced using GIS technology and submitted in both hard copy and digital format.  Maps must indicate the following features, activities and locations:

  - Map Scale- Must be adequate to ensure a clear representation of the proposed corridor.  Multiple maps may be provided to cover the full length of the acreage/corridor.

  - Property Boundary Lines- maps must show parcel boundaries, property lines and owners names for lands adjacent to the Department’s property that is impacted by the project.

  - Surface Disturbance- Areas with the surface disturbance must be identified on the map. This includes, but is not limited to, areas impacted by trenching, clearing, access roads, boring pits and other activities.  Also, the path underground bores should be identified on the map.

  - Dimensions- The map should identify in feet the length and width of the corridor.  It should also include in inches the diameter of the pipeline(s) or utility line(s).

  - Temporary and Permanent Proposed Licensed Areas- These areas should be delineated on the map and dimensions included.  These two areas will be described in a licensed agreement.

  - Labeled intersection- Each map should contain at least one road intersection in close proximity to the proposed project.

  - Pipelines or Utility Lines- The route of the pipeline(s) or utility line(s) must be indicated within the corridor.  This includes the number of lines and the configuration of the lines.  The distances between lines and the width and length of the corridor should be indicated in feet.

  - Products or commodities- The map should indicate the product or commodity being carried within each pipeline or conduit.

- Submission of Required Reports and Plans. The following reports and plans are to be submitted by the applicant and are required for Department and non-Department reviewers.  Additional reports may be required based on the impacted lands and other agency requirements.  A brief description and requirements are listed below:

  - Environmental Assessment-  A trained and credentialed biologist must conduct an environmental assessment of the impacted areas within and potentially outside of the project area.  (Include name and contact information in report)

  - Historic Property Review- Applicant is responsible for submitting its plans and maps to the Historical Society for review and obtaining a concurrence letter indicating that the project will have no significant impact on any cultural or historical resources.

  - Construction Plan- The construction plan must follow the Department’s Best Management Practices and include, but is not limited to, the following information:

    - Start and Completion dates

    - Equipment used on site

    - Road access locations and construction (temporary or permanent)

    - Depth of trenching/boring

    - Location and size of boring pits

    - Ground Clearing activity

    - Removal of Debris

    - Other construction activity as required.

  - Restoration Plan- The restoration plan must follow the Department’s Best Management Practices and include, but is not limited to, the following information:

    - Time of year

    - Grading plans

    - Seeding mixtures and plantings

    - Water and erosion control measures

    - Other restoration measures as required.

  - Post Construction Access and Maintenance Plan- A full description of the operations involving the pipeline corridor must be provided.  This plan must follow the Department’s Best Management Practices and include, but is not limited to, the following information:

    - Permanent road access and maintenance

    - Use of signs and fences

    - Mowing

    - Seeding and plantings

    - Inspections

- Application Fee.  All submissions must be accompanied by a $5,000.00 non-refundable application fee.  Checks are to be made out to:  “Treasurer, State of Ohio”

Any questions regarding the submission of required information and documents can be directed to Tara Paciorek by email at tara.paciorek@dnr.state.oh.us or by phone at

(614) 265-6661.