## Slide 1: ODOT Safety committee• April 25, 2024
Notes: Welcome and Intro

## Slide 2: LIC-SR16-0.20 Safety funding application ODOT District 5
Josh Otworth, PE – ODOT District 5
Alan Haines, PE – City of Pataskala
Andrew Walton, PE – Singh & Associates, Inc.
Scott Knebel, PE – Crawford, Murphy & Tilly

## Slide 3: PURPOSE
Mitigate safety issues at the intersection of SR 16 (E. Broad Street) and Taylor Rd (TR 169) – 24% injury crashes in 5 years (2018-2022)
Meets Ohio Emphasis Area: High Risk Drivers (47.3% of crashes involved young drivers)
Meets FHWA Emphasis Area: Improving the design and operation of intersections

## Slide 4: Area map

## Slide 5: Existing conditions
Sight distance of left turning vehicles on SR 16 approaches adversely affected by EB lane drop and WB added through lane.
Driveways within functional area of intersection contribute to angle and left turn crash patterns.
Central Ohio Technical College located on NW quadrant of the Taylor Road (TR 169) intersection.
Previous countermeasures (backplates, clearance intervals) did not mitigate crashes.

## Slide 6: operational concerns
Multiple factors contribute to safety performance (signalized intersection, stopping sight distance/vertical curve, access mgt).
EB SR 16 approach
East leg - No Crosswalk

## Slide 7: Crash summary
112 total crashes (2018-2022)
Serious ped crash within unmarked crosswalk (east leg)
33 injury crashes resulting in a 27% injury rate
Left turning (21.3%) and angle (23%) crashes contribute to severity
All crashes occurred within the functional area of the intersection

## Slide 8: Recommended countermeasures
Extend second EB through lane east of Taylor Road, install an eastbound right turn lane (385 feet) with upgraded overhead signing, and positive offset LT lanes
Install pedestrian facilities on the north, east, and south legs (marked crosswalks, ped heads, and ADA ramps)
Add backplates to signal heads w/provisions for future FYA sequence
Close north access to Circle K, convert east access to RIRO, and close west access to Licking Line Plaza

## Slide 9: Recommended Countermeasures (CONCEPT PLAN)
Broad St (SR 16)
Taylor Rd (TR 169)

## Slide 10: Engineer’s opinion of probable cost

## Slide 11: Funding summary

## Slide 12: Scoring (32 points)
Ratio observed fatal/serious injuries to observed totals (2 pts) = 0.01
% of the Potential for Safety Improvement to Total Expect crashes (8 pts)= 11.01%
Relative severity index (10 pts) = 31,599
Equivalent PDO Index (10 pts) = 3.06
Location Equity Measure (2 pts) = 15%

## Slide 13: Benefit cost ratio (0.87)
CMFs applied for sign/signal upgrades and for access modifications.
No CMFs applied for sight distance improvements (offset LT lanes) or capacity improvements -- both are contributing factors.

## Slide 14: Project schedule

## Slide 15: Questions
?
Last updated 3/11/2024