# V– GENERAL

## Channel

The Cuyahoga River passes under the main steel span at an approximate skew of 65 degrees.  An underwater investigation performed by Lake Erie Diving has found the river channel bottom to be in good condition.  See Appendix C.

- Approaches

East approach and west approaches are in good condition. Minor cracking in the asphalt approaches was observed.  A depression in the east approach asphalt pavement was also noted.

- Land Use

In addition to the Cuyahoga River passing under Span 4, several other areas under the bridge are utilized.  On the West side of the river, Riverbed Road passes under Span 2.  The area under Span 3 was being backfilled during the inspection.  On the East side of the river, parking lots are located under Spans 5, 6, 8, and 9.  West Avenue and Merwin street pass under Span 7.  A pedestrian walkway is located under Span 10 and a RTA rapid line runs under Span 11 (see Photo 21, page 20).  Robert Lockwood Jr. Drive passes under Span 12 (see Photo 22, page 20).

- Navigation Lighting

The navigation lights on the structure are operating properly.

- Structure and Architectural Lighting

During the bridge inspection, a lighting contractor was replacing several decorative lights.  A night inspection of the lighting found the structure and architectural lighting to be in good working condition.