## Slide 1: Cost Estimating Workshop March 14-17, 2011

## Slide 2: Project Phase Update
Phase 1 and 3
Brad Hyre, P.E.
Transportation Manager
HDR
Phase 2
Manoj Sethi, P.E.
Executive Vice President
DLZ

## Slide 3: Phase 2 C.R. 28 to U.S. 23
Typical Section

## Slide 4: Typical Section

## Slide 5: Roadway Design
Horizontal Alignment (No change)
Vertical Alignment (Significant change)
Interchanges (Refinement)

## Slide 6: Interchanges
Lucasville-Minford Rd (CR 28)

## Slide 7: Interchanges
US 23

## Slide 8: Utilities
Relocations Expected
AEP Transmission – 138KV facility (near STA 857+20)
Electric Dist. Line along CR-28, CR-29, CR-54, Flatwood Fallen Timber Road, Fairgrounds Road and R/R Tracks
Water, Gas & Sanitary Lines run parallel along Fairgrounds Road

## Slide 9: Geotechnical
Bridge foundations
  Spread footings
  Driven piles
  Drilled shafts

## Slide 10: Geotechnical
Embankments
  High fills
  Soft soils
    May require 3H:1V slopes, staged construction
      US 23 Interchange
      Lucasville-Minford Road Interchange

## Slide 11: Geotechnical
Embankments (cont’d)
  Special benching for sidehill fills
  Embankment materials mostly rock
  Durable rock at base of embankments for drainage

## Slide 12: Geotechnical
Cut Slopes
  Cut slopes higher than 150 feet
    0.5H:1V cut slopes in competent sandstone
    1H:1V cut slopes in weathered rock
    2H:1V cut slopes in weak rock and overburden
  Benches
    Construction deviation benches every 60’ vertical
    Overburden benches
    Geotechnical benches

## Slide 13: Geotechnical
Cut Slopes (cont’d)

## Slide 14: Geotechnical
Cut Slopes (cont’d)
  Catchment ditches for rockfall
    Several different options proposed

## Slide 15: Geotechnical
Cut Slopes (cont’d)

## Slide 16: Geotechnical
Cut Slopes (cont’d)

## Slide 17: Structures
10 Structures in this Phase

## Slide 18
SCI-823-MAINLINE 4 bridges
Bridge No. | Bridge Description | Structure Type | Estimated Cost
1018 L&R | S.R. 823 over Lucasville-Minford Road L/R (VC = 28.83 feet) | 3-span prestressed concrete 60” I-beam with integral abutments, cap and column piers | $3,978,000
1096 L&R | S.R. 823 over Blue Run (CR-29) L/R (VC = 40.0 feet) | Single span prestressed 60” I-Beam on semi-integral abutments w/MSE wall supported abutments | $2,656,000
1357 L&R | S.R. 823 over Morris Lane Blue Run Road L/R (VC = 52.0 feet) | 5-span prestressed I-Beam with semi-integral abutments and T-type piers on spill thru slopes | $10,838,000
1431 | S.R. 823 Under Flatwood-Fallen Timber Road (CR-184) (VC = 71.0 feet) | 2-span steel plate girders with semi-integral abutments on spill thru slopes (1:1) | $3,012,800
 |  | Total | $20,484,800

## Slide 19: Morris Lane -Blue Run
Significant change to this Design is proposed

## Slide 20
US 23 INTERCHANGE: 6 Bridges & MSE Walls
Bridge No. | Bridge Description | Structure Type | Estimated Cost
1593 | Ramp B over Fairground Road (C.R. 55) | Single-span prestressed concrete with semi-integral abutments behind MSE walls | $542,000
1598 | Ramp B over Norfolk Southern Railway | 3-span steel plate girders with conventional stub abutments. A pill thru slope is used at forward abutment, rear abutment is behind an MSE wall supported by Geopiers | $3,205,000
1594 | S.R. 823 over Fairground Road (C.R. 55) | Single-span prestressed concrete beams with semi-integral abutments behind MSE walls | $1,046,000
1601 | S.R. 823 over Norfolk Southern Railway and US 23. | 3-span steel plate girders with semi-integral abutments behind MSE walls | $3,186,000

## Slide 21
US 23 INTERCHANGE (contd.)
Bridge No. | Bridge Description | Structure Type | Estimated Cost
1595 | Ramp C over Fairground Road (C.R. 55) | Single-span prestressed concrete beam with semi-integral abutments behind MSE walls | $583,000
1603 | Ramp C over Norfolk Southern Railway | 3-span steel plate girders with conventional stub abutments. A spill thru slope is used at the rear abutment and the forward abutment is behind an MSE wall supported by Geopiers | $3,655,000
Walls |  | 6 MSE Walls at the Interchange. Geopiers for Ramp B and C | $5,674,400
 |  | Total | $17,891,400

## Slide 22: S.R. 823 over NS Railway and US 23

## Slide 23: Hydraulics
Open drainage system using culverts and ditches
Closed drainage systems using catch basins, manholes and storm sewers
Culverts range from 36-in. to 72-in.
10’x5’ Box under U.S. 23
Length of culverts up to 900-ft.
Height of fill above some culverts up to 120-ft.