## Slide 1: Ohio DOT CADD Users Group – Aug. 27th, 2025
Office of CADD & Mapping Services

## Slide 2: House Keeping Items
CPDs only available to in-person attendees
  Make sure you signed in at the table right outside the auditorium (getting a badge to get into the building does not sign you into this event)
  CPDs email out by end of the week
Online attendees should be using teams for video/audio.
  Please mute yourself
  Please use the chat to ask questions
Recording will be posted by end of the week on wiki
https://bentleysystems.service-now.com/community?id=kb_article_view&sysparm_article=KB0046180

## Slide 3: Welcome and Updates
John Drsek PE, ODOT CADD & Mapping Services

## Slide 4: Agenda

## Slide 5: BIM Projects-Update
John Drsek PE, ODOT CADD & Mapping Services

## Slide 6: BIM Strategic Plan
BIM Strategic plan published August 1st, 2024
https://www.transportation.ohio.gov/programs/bim

## Slide 7: ODOT W.O.R.K.S.
Workflow Optimization for Real-time Knowledge Sharing
Project Manager: Rachel Lewis
Other Project Lead: Eric Kahlig
Construct
Design
BID

## Slide 8: Project Description
The Ohio Department of Transportation (ODOT), in collaboration with industry partners, will elevate the iModel by developing workflows and technology connectors to harness open-source data infrastructure, enabling efficient management and transfer of digital data through its lifecycle.

## Slide 9: Project Team

## Slide 10: Key initiatives
Accelerating the deployment of model technology.
Provide a testing sandbox to provide a real-time feedback loop without disruption to projects and with more timely results.
Provide free and accessible model information when/where required.
Consumption of iModel through the design & construction phases of the lifecycle.
Provide the foundation to move technology to the ability to sign & seal models.
Create model fidelity to allow model as the contract document.

## Slide 11: Project Goals
GOAL 5: Additional iModel Use Cases/Implementation Opportunities
Engage stakeholders to gather use cases.
Evaluate best applications and/or processes to provide the iModel to meet use case needs.
Pilot use cases and make recommendations.
Public involvement, safety in work zones, stakeholders…
Review of current workflow & technology and make recommendations
Model review application with needed enhancements & configurations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Current tools lack what's needed to perform adequate design reviews of 3d models.
GOAL 1: iModel Review in Design
GOAL 2: Open-Source Bidding
Review of current workflow & technology and make recommendations
Workflow and viewer for externals to have free, unauthenticated access (accessible to the public)
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently no mechanism to provide the iModel during letting that is free, open source and Open access.
GOAL 3: iModel for Construction Inspection
Review of current workflow & technology and make recommendations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently ODOT still utilizes contractor provided models for construction inspection.
Have ODOT process of quality attribute inspection requirements and validation results interface through the 3D model
GOAL 4: iModel for Construction Consumption
Invite stakeholders to test equipment in sandbox.
Create workflow for iModel consumption and contracting.
Provide training.
Currently contractor creates their own 3d model from 2d plans
Issues with model fidelity and “trust” in the models.
Lack of interoperability between applications and equipment.
Gaps in skillsets and comfortability
Demonstrate how iModel can alleviate some hurdles, document benefits, and make recommendations for the industry to accelerate adoption.

## Slide 12: Project Goals
GOAL 5: Additional iModel Use Cases/Implementation Opportunities
Engage stakeholders to gather use cases.
Evaluate best applications and/or processes to provide the iModel to meet use case needs.
Pilot use cases and make recommendations.
Public involvement, safety in work zones, stakeholders…
GOAL 1: iModel Review in Design
Review of current workflow & technology and make recommendations
Model review application with needed enhancements & configurations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Current tools lack what's needed to perform adequate design reviews of 3d models.
GOAL 2: Open-Source Bidding
Review of current workflow & technology and make recommendations
Workflow and viewer for externals to have free, unauthenticated access (accessible to the public)
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently no mechanism to provide the iModel during letting that is free, open source and Open access.
GOAL 3: iModel for Construction Inspection
Review of current workflow & technology and make recommendations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently ODOT still utilizes contractor provided models for construction inspection.
Have ODOT process of quality attribute inspection requirements and validation results interface through the 3D model
GOAL 4: iModel for Construction Consumption
Invite stakeholders to test equipment in sandbox.
Create workflow for iModel consumption and contracting.
Provide training.
Currently contractor creates their own 3d model from 2d plans
Issues with model fidelity and “trust” in the models.
Lack of interoperability between applications and equipment.
Gaps in skillsets and comfortability
Demonstrate how iModel can alleviate some hurdles, document benefits, and make recommendations for the industry to accelerate adoption.

## Slide 13: Project Goals
GOAL 5: Additional iModel Use Cases/Implementation Opportunities
Engage stakeholders to gather use cases.
Evaluate best applications and/or processes to provide the iModel to meet use case needs.
Pilot use cases and make recommendations.
Public involvement, safety in work zones, stakeholders…
GOAL 1: iModel Review in Design
Review of current workflow & technology and make recommendations
Model review application with needed enhancements & configurations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Current tools lack what's needed to perform adequate design reviews of 3d models.
GOAL 2: Open-Source Bidding
Review of current workflow & technology and make recommendations
Workflow and viewer for externals to have free, unauthenticated access (accessible to the public)
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently no mechanism to provide the iModel during letting that is free, open source and Open access.
GOAL 3: iModel for Construction Inspection
Review of current workflow & technology and make recommendations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently ODOT still utilizes contractor provided models for construction inspection.
Have ODOT process of quality attribute inspection requirements and validation results interface through the 3D model
GOAL 4: iModel for Construction Consumption
Invite stakeholders to test equipment in sandbox.
Create workflow for iModel consumption and contracting.
Provide training.
Currently contractor creates their own 3d model from 2d plans
Issues with model fidelity and “trust” in the models.
Lack of interoperability between applications and equipment.
Gaps in skillsets and comfortability
Demonstrate how iModel can alleviate some hurdles, document benefits, and make recommendations for the industry to accelerate adoption.

## Slide 14: Project Goals
GOAL 5: Additional iModel Use Cases/Implementation Opportunities
Engage stakeholders to gather use cases.
Evaluate best applications and/or processes to provide the iModel to meet use case needs.
Pilot use cases and make recommendations.
Public involvement, safety in work zones, stakeholders…
GOAL 1: iModel Review in Design
Review of current workflow & technology and make recommendations
Model review application with needed enhancements & configurations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Current tools lack what's needed to perform adequate design reviews of 3d models.
GOAL 2: Open-Source Bidding
Review of current workflow & technology and make recommendations
Workflow and viewer for externals to have free, unauthenticated access (accessible to the public)
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently no mechanism to provide the iModel during letting that is free, open source and Open access.
GOAL 3: iModel for Construction Inspection
Review of current workflow & technology and make recommendations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently ODOT still utilizes contractor provided models for construction inspection.
Have ODOT process of quality attribute inspection requirements and validation results interface through the 3D model
GOAL 4: iModel for Construction Consumption
Invite stakeholders to test equipment in sandbox.
Create workflow for iModel consumption and contracting.
Provide training.
Currently contractor creates their own 3d model from 2d plans
Issues with model fidelity and “trust” in the models.
Lack of interoperability between applications and equipment.
Gaps in skillsets and comfortability
Demonstrate how iModel can alleviate some hurdles, document benefits, and make recommendations for the industry to accelerate adoption.

## Slide 15: Project Goals
GOAL 5: Additional iModel Use Cases/Implementation Opportunities
Engage stakeholders to gather use cases.
Evaluate best applications and/or processes to provide the iModel to meet use case needs.
Pilot use cases and make recommendations.
Public involvement, safety in work zones, stakeholders…
GOAL 1: iModel Review in Design
Review of current workflow & technology and make recommendations
Model review application with needed enhancements & configurations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Current tools lack what's needed to perform adequate design reviews of 3d models.
GOAL 2: Open-Source Bidding
Review of current workflow & technology and make recommendations
Workflow and viewer for externals to have free, unauthenticated access (accessible to the public)
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently no mechanism to provide the iModel during letting that is free, open source and Open access.
GOAL 3: iModel for Construction Inspection
Review of current workflow & technology and make recommendations
Invite stakeholders to test in sandbox
Training and Knowledgebase Documentation
Currently ODOT still utilizes contractor provided models for construction inspection.
Have ODOT process of quality attribute inspection requirements and validation results interface through the 3D model
GOAL 4: iModel for Construction Consumption
Invite stakeholders to test equipment in sandbox.
Create workflow for iModel consumption and contracting.
Provide training.
Currently contractor creates their own 3d model from 2d plans
Issues with model fidelity and “trust” in the models.
Lack of interoperability between applications and equipment.
Gaps in skillsets and comfortability
Demonstrate how iModel can alleviate some hurdles, document benefits, and make recommendations for the industry to accelerate adoption.

## Slide 16
ADCMS ODOT W.O.R.K.S. PROJECT SCHEDULE

## Slide 17
ADCMS Federal Authorization
January 29, 2025
In-person stake holder engagement March 18, 2025
Included ODOT, MDOT, MinnDOT, Consultants, Bentley.
Went over current paper/pdf review process to identify understanding of process/lack of functionality with current iModel review tools.
A lot of differences in current review processes across the state/lack of consistency.

## Slide 18
Sandbox setup
March-June 2025
ODOT’s PW DS to Bentley Infrastructure cloud
Use to provide real-time feedback loop, won't disrupt projects
12 Projects, want to capture review for all project types even non-modeled projects
Ranging from DDI to culvert replacements to resurfacings.
Struggling to set up data for staged reviews as projects were already at final stage.
Consultant Assistance Contract Announcement
May 5, 2025
LOI: 5/27/2025, Selection: 6/27/2025
Workflow documentation
Identify Best practices
Develop training content
Stakeholder engagement assistance
Federal Authorization
January 29, 2025
In-person stake holder engagement March 18, 2025
Included ODOT, MDOT, MinnDOT, Consultants, Bentley.
Went over current paper/pdf review process to identify understanding of process/lack of functionality with current iModel review tools.
A lot of differences in current review processes across the state/lack of consistency.

## Slide 19
Sandbox setup
March-June 2025
ODOT’s PW DS to Bentley Infrastructure cloud
Use to provide real-time feedback loop, won't disrupt projects
12 Projects, want to capture review for all project types even non-modeled projects
Ranging from DDI to culvert replacements to resurfacings.
Struggling to set up data for staged reviews as projects were already at final stage.
Consultant Assistance Contract Announcement
May 5, 2025
LOI: 5/27/2025, Selection: 6/27/2025
Workflow documentation
Identify Best practices
Develop training content
Stakeholder engagement assistance
Federal Authorization
January 29, 2025
In-person stake holder engagement March 18, 2025
Included ODOT, MDOT, MinnDOT, Consultants, Bentley.
Went over current paper/pdf review process to identify understanding of process/lack of functionality with current iModel review tools.
A lot of differences in current review processes across the state/lack of consistency.

## Slide 20
Get Consultant under contract
Micheal Baker, HDR, GFT team
Support decisions with input and experimentation.
Develop workflows and training
Provide workforce training and upskilling
Change management practices
Refine review processes
Continue to work on identifying design review processes that need replicated/replaced within iModel review.
2nd phase Scoping and Planning with Bentley
Goal 1: (iModel design review)
Goal 2: (iModel opensource/open access bidding)
Goal 3: (iModel construction inspection)
Sandbox setup
March-June 2025
ODOT’s PW DS to Bentley Infrastructure cloud
Use to provide real-time feedback loop, won't disrupt projects
12 Projects, want to capture review for all project types even non-modeled projects
Ranging from DDI to culvert replacements to resurfacings.
Struggling to set up data for staged reviews as projects were already at final stage.
Consultant Assistance Contract
May 5, 2025
LOI: 5/27/2025, Selection: 6/27/2025
Workflow documentation
Identify Best practices
Develop training content
Stakeholder engagement assistance
Timeline – current

## Slide 21: ADCMS
Working on getting monthly reports posted to our website.

## Slide 22: BIM Projects
Model As a Legal Document/Deliverable (MALD) Research Project: July 2025 – January 2027
  Exploring the Technological, Implementation, and Legislative Pathways for ODOT
  Consultant: HNTB Selected

## Slide 23: Bim Projects
Consultant Contract: Future Programmatic
  9/8/2025 – STW CADD BIM & Model Development
  Assist the Department with improving BIM capabilities by aiding in the development and implementation of ORD Drainage & Utilities Analytics, OBM, provide workspace development and support, support continued model development, support ADCMS activities, and develop training materials as needed.

## Slide 24: Bim Projects
Estimation
  Implementation Kickoff 8-26-2025
  Apart of AASHTOWare Project Modules
  Replaces Estimator
  Web-based
  Allows for better data flow and more integrations
    Asset Tracker and Quantimate.

## Slide 25: BIM Projects
Progressive Design-Build BIM Pilot WOO-23
  March 2024 - Oct. 2025
  Design Build Team: Kokosing Construction Co./Michael Baker International
  Build framework for BIM Execution Plan
  Planless
  Construction Started Aug. 4th!

## Slide 26: BIM Projects
Developing Level of Development (LOD) and Model Element Breakdown (MEB) standards/guidelines
  Oct. 2024-June 2025
  Consultant: Michael Baker International

## Slide 27: BIM PROJECTS
Tech. Stack Gap Analysis
  May 2024 - June 2025
  Consultant: Geo Decisions
  Map existing data and connections or lack there of across asset lifecycle
  (i.e. Planning, Design, Estimating, Contracts, Bidding, Construction, Inspection, Asset Management, As-builts).

## Slide 28: Updates-Blueprints
  OpenBridge: On hold due to staffing changing in OSE.
  ORD Drainage Analytics: On hold due to staffing changes in OHE.
  OpenGround ORD Extension: On hold due to bug preventing Moisture content from importing.

## Slide 29: L&D vol 3 Updates-plan set update
Fixed various links throughout document.
Added clarification to digital signature process for Right of Way Sheets

## Slide 30: L&D vol 3 Updates-plan set update
Added clarification for when LandXML files are to be included with supporting documents
Surveyor Report updated to say Survey Master
Updates & Archive | Ohio Department of Transportation

## Slide 31: L&D Vol 3 Plan Set Reminders
Each PID should only have 1 planset pdf.
YouTube Video: Plan Set Components
This includes multi part projects being filed under a single PID:
[CTY]-[PID]-PlanSet.pdf
  [CTY]-[PID]-Plan_Part[#].pdf
  [CTY]-[PID]-Plan-RW_Part[#].pdf
  [CTY]-[PID]-Signatures_Part[#].pdf
  [CTY]-[PID]-SP-[Desc].pdf
[CTY]-[PID]-PlanSet.pdf
  [CTY]-[PID]-Plan.pdf
  [CTY]-[PID]-Plan-RW.pdf
  [CTY]-[PID]-Signatures.pdf
  [CTY]-[PID]-SP-[Desc].pdf

## Slide 32: ORD Versions and ODOTCEv02 WorkSpace
Last ODOTCEv02 WorkSpace Update: July 23rd, 2025
  A couple dgnlibs were updated to ORD 2024 civil schema.
    This makes it incompatible with ORD 10.12 (as well as ORD 2023)
    Sync Tool has version control to maintain compatibility
    Zip downloads

## Slide 33: ORD Versions
Just starting testing ORD 2024 (24.00.02.25)
  This is a minor update and does not have a civil schema change, so this is not a compatibility issue with v24.00.00.205.
As always, your free to move to this version before ODOT.
  Just make sure everyone working a given project is using a version with the same civil schema.
  Reminder that ODOTS PW DS will only work with ORD 2024 or newer.
    If your running older versions of ORD you WILL see problems.

## Slide 34: Running Update Doc Format Change
We are working on switching our running updates document to excel.
  This document outlines all the changes we have made to our workspace
  More granularity, more information, more functionality (filtering, sorting)

## Slide 35: Transoft Part 1 (Torus OHDOT Example)
Andrew Holloway P.E., ODOT Office of Roadway Engineering
Janz Arqueza, Transoft Solutions

## Slide 36: Project Location
Intersection of SR-73 & SR-503 in Butler County (District 8)

## Slide 37: Project Location

## Slide 38: Project Background

## Slide 39: Project Details
Route | Functional Class | ADT | Truck % | Traffic Control
SR-73 | Minor Arterial | 6046 vpd | 8% | Flashing Yellow Intersection Control Beacon
SR-503 | Major Collector | 2907 vpd | 4% | Stop Controlled/ Flashing Red Intersection Control Beacon

## Slide 41: Fastest Path Checks

## Slide 42: Establish constraints

## Slide 45: Vertical Geometry
North
West
East
South

## Slide 46: Vertical Geometry

## Slide 48: Torus Linework

## Slide 49: Proposed Linework

## Slide 50: Concept Plan

## Slide 51: Discussion with Transoft

## Slide 52: Networking Break 1
Don’t be this guy

## Slide 53: Transoft Part 2 (Torus Tutorial)
Transoft

## Slide 54: Transoft Part 3 (AQCESSRamp DeMO)
Transoft

## Slide 55: Lunch Break

## Slide 56: SUE Level Standards
John Drsek, PE

## Slide 57: L&D V4 (2200 Subsurface Utility Locations Specification)
Ohio DOT Specification
  Housed in L&D V4
    Formerly called “Subsurface Utility Location Services Specifications”
    Based on ASCE 38-22
      Standard Guideline for Investigating and Documenting Existing Utilities

## Slide 58: ASCE 38-22
Utility Quality Levels Overview
  Emphasizes risk management, data reliability, and professional accountability.
  Introduces a model-based approach to utility data.
Quality Level
QL-D: Derived from records or verbal recollections.
QL-C: Correlated with visible surface features.
QL-B: Determined using surface geophysical methods.
QL-A: Verified by direct exposure.

## Slide 59: Quality Levels in OHDOTCEv02
New/Updated Field Codes
  Split out Overhead and Underground
    Underground Receives Quality
Field Code | Description
OCTVL | Overhead Cable TV Line
OFO | Overhead Fiber Optic
OPL | Overhead Power Line
OTL | Overhead Telephone Line
OCL | Overhead Combined Line Utility
UCTVL | Underground Cable TV Line
UFO | Underground Fiber Optic
UPL | Underground Power Line
UTL | Underground Telephone Line
GL | Gas Line
WL | Water Line
Old Field Code
CTVL
FO
PL
TL

## Slide 60: Quality Levels in OHDOTCEv02
How do quality levels get assigned?
  Attributes
    Underground Quality level-based codes have a new attribute field for Quality
      Default Quality is D if not entered into the survey import.

## Slide 61: Example data with the new codes (Csv)
Point | Northing | Easting | Elevation | Code | Attribute Name | Attribute Value | Attribute Name | Attribute Value | Attribute Name | Attribute Value | Attribute Name | Attribute Value | Attribute Name | Attribute Value
SV001 | 1020 | 1000 | 1000 | OCTVL BL* | TYPE | Conventional | NOTE | TEST Note |  |  |  |  |  | 
SV002 | 1020 | 1200 | 1000 | OCTVL EL* | TYPE | Conventional | NOTE | TEST Note |  |  |  |  |  | 
SV003 | 1030 | 1000 | 1000 | UCTVL BL* | QUALITY LEVEL | A | TYPE | Fiberoptic | NOTE | TEST Note |  |  |  | 
SV004 | 1030 | 1200 | 1000 | UCTVL EL* | QUALITY LEVEL | A | TYPE | Fiberoptic | NOTE | TEST Note |  |  |  | 
SV005 | 1040 | 1000 | 1000 | OFO BL* | NOTE | TEST Note |  |  |  |  |  |  |  | 
SV006 | 1040 | 1200 | 1000 | OFO EL* | NOTE | TEST Note |  |  |  |  |  |  |  | 
SV007 | 1050 | 1000 | 1000 | UFO BL* | QUALITY LEVEL | C | NOTE | TEST Note |  |  |  |  |  | 
SV008 | 1050 | 1200 | 1000 | UFO EL* | QUALITY LEVEL | C | NOTE | TEST Note |  |  |  |  |  | 
SV009 | 1060 | 1000 | 1000 | OPL BL* | VOLTAGE | 14400 | NOTE | TEST Note |  |  |  |  |  | 
SV010 | 1060 | 1200 | 1000 | OPL EL* | VOLTAGE | 14400 | NOTE | TEST Note |  |  |  |  |  | 
SV011 | 1070 | 1000 | 1000 | UPL BL* | QUALITY LEVEL | C | VOLTAGE | 7200 | NOTE | TEST Note |  |  |  | 
SV012 | 1070 | 1200 | 1000 | UPL EL* | QUALITY LEVEL | C | VOLTAGE | 7200 | NOTE | TEST Note |  |  |  | 
SV013 | 1080 | 1000 | 1000 | GL BL* | QUALITY LEVEL | C | MATERIAL | Polyethylene | PRESSURE | 40 PSIG | NOTE | TEST Note |  | 
SV014 | 1080 | 1200 | 1000 | GL EL* | QUALITY LEVEL | C | MATERIAL | Polyethylene | PRESSURE | 40 PSIG | NOTE | TEST Note |  | 
SV015 | 1090 | 1000 | 1000 | OTL BL* | TYPE | Conventional | NOTE | TEST Note |  |  |  |  |  | 
SV016 | 1090 | 1200 | 1000 | OTL EL* | TYPE | Conventional | NOTE | TEST Note |  |  |  |  |  | 
SV017 | 1100 | 1000 | 1000 | UTL BL* | QUALITY LEVEL | B | TYPE | Fiberoptic | NOTE | TEST Note |  |  |  | 
SV018 | 1100 | 1200 | 1000 | UTL EL* | QUALITY LEVEL | B | TYPE | Fiberoptic | NOTE | TEST Note |  |  |  | 
SV019 | 1110 | 1000 | 1000 | WL BL* | SIZE | 6" | QUALITY LEVEL | D | MATERIAL | Ductile Iron | PRESSURE | 40 PSIG | NOTE | TEST Note
SV020 | 1110 | 1200 | 1000 | WL EL* | SIZE | 6" | QUALITY LEVEL | D | MATERIAL | Ductile Iron | PRESSURE | 40 PSIG | NOTE | TEST Note
SV021 | 1130 | 1000 | 1000 | OCL BL* | TYPE | Electric and Cable | NOTE | TEST Note |  |  |  |  |  | 
SV022 | 1130 | 1200 | 1000 | OCL EL* | TYPE | Electric and Cable | NOTE | TEST Note |  |  |  |  |  | 

## Slide 62: Summary
New Codes
New Attribute
New Levels
New Linestyles
add U for underground, O for Overhead
Quality level
to indicate Quality level
UT_X_FO_QLA, UT_X_FO_QLB…
to indicate quality level
If missing then quality level D is used as default
Old codes (CTVL, FO, TL, PL) removed from code list for collectors.
BUT dgnlib (survey settings) still has old codes (feature definitions) for processing
Might need to update standards from DGNLIB if going back to previous field book dgn files.

## Slide 63: Bonus field codes!
New Field Codes
  PMTS
    Pole Mounted Traffic Sensor
  FLD
    Cultivated Field
  WALLN
    Noise Wall
  EOW
    Edge of Water
  AUTOMATIC & MANUAL
    Added for mobile mapping control use

## Slide 64: Where are the code lists?
L&D V4 Webpage or the OHDOTCEV02 Standards
  Webpage
    https://www.transportation.ohio.gov/working/engineering/cadd-mapping/location-design-vol-4
  OHDOTCEV02
    \..\Standards\Survey Files\Field Codes\
CATEGORY | CODE | DESCRIPTION | CELL | ATTRIBUTES | DTM | SHOT LOCATION
AERIAL TARGETS | AERLCH | Aerial Lidar Check Shot Hard | Default "+" | Shot Location | DNI | 
AERIAL TARGETS | AERLCS | Aerial Lidar Check Shot Soft | Default "+" | Shot Location | DNI | 
AERIAL TARGETS | AERPP | Aerial Photo Point | VCTRL | Note1 - any notes Note2 Note3 | DNI | The desired photo point.
AERIAL TARGETS | AERTAR | Aerial Target Full | FCTRL | Target# | DNI | The center of the target.
Updated Excel Sheet

## Slide 65: Defects/Issues
John Drsek, PE

## Slide 66: Defects/Issues
Merge to Master dropping cells
  Only going from 3d model to 2d model
  Workaround 1: Export > 2d.
  Workaround 2: use Copy/paste tools instead
  Introduced in ORD 24.0.0.205
  Fixed in ORD 24.0.2.25

## Slide 67: Defects/issues
Snapping geometry to survey points toggles survey display off
  Workaround 1: Turn off persist snaps before snapping to points.
  Workaround 2: Turn points back on after snapping. (Survey Details)
  Scheduled to be fixed in ORD 2025

## Slide 68: Defects/issues
Can’t Edit Parametric Cells
  IN ORD 2024 the variables are not shown, so no way to change them
    Not an issue in MicroStation
  Workaround: edit the cell definition directly to create a new variation

## Slide 69: Defects/Issues
Can’t Edit Parametric Cells Cont.
Fixed in ORD 2025

## Slide 70: Defects/Issues
Reminder: There are two cel files for parametric cells due to a bug introduced in ORD 10.12.
  OHDOT_3D_Headwalls.cel (only use if in ORD 10.10 or earlier)
  OHDOT_3D_Headwalls_ORD1012.cel (use if in ORD 10.12 or newer)
We plan on renaming this files in a future update
  OHDOT_3D_Headwalls.cel  OHDOT_3D_Headwalls_ORD1010.cel
  OHDOT_3D_Headwalls_ORD1012.cel  OHDOT_3D_Headwalls.cel

## Slide 71: Defects/Issues
Drainage Conduit Symbology Problems (Default level)
    Dependent on feature definition
      Type-B-Round Metal CL-P
        Shows center of pipe, not extents
      Type-B-Round Metal-P
        Shows extents of pipe, not center
    Workaround: select elements and set level manually
View | Correct Level? | 
 | Conduit Feature | 
 | CL | Extents
Plan | ✔ | ✘
Profile | ✘ | ✘
Profile Run | ✘ | ✘
Projected Profile | ✔ | ✘
Profile Connected Conduit | ✔ | ✘
Profile 3D cut | ✔ | ✔
XS | ✔ | ✔
3D | ✔ | ✔

## Slide 72: Defects/Issues
Outgoing Conduit Angle Changed by 180 degrees
  The DU Item Type Sync app uses this angle to figure out the cardinal direction of the pipe from the node (North, North West, West…)
  In ORD 2024, the Outgoing conduit angle is now reporting 180 degrees more then it did in ORD 10.12.
    This results in the cardinal direction for outgoing conduit to be incorrect (Example a pipe going East would incorrectly show West as the direction)
  The other conduit angle properties remain unchanged.

## Slide 73: Defects/Issues
    Angle property is only updated when node is changed, not just by opening a file, can’t assume angle is from 10.12 or 24
  Why not update the DU sync app to account for this based on running version?
Outgoing Conduit Angle Changed by 180 degrees Cont.
  Target to fix back in ORD 2025
  Workaround: use DU Item Type Sync app to manually override value
Angle (°) | Cardnal Direction
0 | East
45 | North East
90 | North
135 | North West
180 | West
225 | South West
270 | South
315 | South East

## Slide 74: Defects/Issues
Outgoing Conduit Angle Changed by 180 degrees Cont.
  DU Item Type Sync App updated to calculate direction directly from the start and end points of the connected conduit.
    Currently only did this for the outgoing conduit direction
    Version 1.0.1.2, pending release
  This also includes an update to the OHDOT_DU Item Type library.
  Once Released, open drainage basemap file and sync OHDOT_DU Item type library. Then open DU sync app and it will calculated the correct direction

## Slide 75: Defects/Issues
Outgoing Conduit Angle Changed by 180 degrees Cont.
  How do I know if it's calculating the new way?
Old Value
New Value

## Slide 76: Defects/Issues
Drainage Pipes not showing in profile 3d Cuts
  Related to fill and color for pipes that have a defined thickness
  DGNLIB was updated to remove the closed linear settings from the Pipe-P element template.
    This fixes the problem from happening in the future
  For existing files
    Remove the closed linear settings form the Pipe-P element template in your dgn file
    You need to change the pipe Feature definition to something else and change it back to fix

## Slide 77: Defects/Issues
Two Named Boundary Dialogs
  Be careful which named boundary dialog you open
    Named boundary from fence tools will open the wrong dialog

## Slide 78: Defects/Issues
Printing shows border around text
  MS update changed some things around printing
    This made our pen tables print masked text with a border
    ODOT updated pen tables to resolve this problem
    If using a copy of ODOT’s pen tables, you need to disable the fill color in the output account
    Or stop using Masked text!

## Slide 79: Defect/Issues
Annoying message if you keep Feature Definition Toolbar docked
  If you have this toolbar docked/opened and you open or switch to a sheet or drawing model you will get this message box.
  Bentley says this is works as design noting product stability.
  So a toolbar that’s meant to be docked..don’t dock to avoid annoying message box.

## Slide 80: Workspace Updates
Joshua Durbin, EI

## Slide 81: Workspace Updates
Update Survey zips with corrections/new codes
OHDOT DU ItemType Sync App
  Major update for ORD 2024
  Huge Performance optimization throughout app (mins to secs)
  Fixed some crashing issues
OHDOT Sheet Manager
  Fixed bug that was preventing file from being copied out if a reference file is checked out

## Slide 82: Workspace Updates
OHDOT_SCD app
  Updated to populate date from FTP site instead of sharepoint site
  Added backup to read SCD date from local workspace if it failed get date from FTP site
OHDOT_Note app
  FIXED NUMLOCK TOGGLE ISSUE!, I REPEAT FIXED NUMLOCK ISSUE!
  Updated to populate data from FTP site instead of sharepoint site
  Fixed backup to read notes data from workspace if failed to get data online

## Slide 83: Workspace Updates
Create Design files app
  Fixed bug that was listing local cached seed files that were deleted from projectwise
  Fixed bug that prevented new files from being created if a file that was deleted is still cached locally.
Indexer App
  Fixed bug that was using document name from PW when creating zip instead of File name
  Fixed bug that was deleting local copy of zip if it failed to upload zip into projectwise.
  NOTE: don’t save to ONEDRIVE location, ongoing security issue

## Slide 84: Workspace Updates
Pen Tables
  Disabled output fill color (fixes issue with masked text printing with border)
  Text Substitution now includes Plot Driver, PenTable, Workspace, Workset, and product name
  Changed username from windows username to the users connect username.
  Fixed Text Substitution for file name to ensure it used the File name and not ProjectWise Document name.

## Slide 85: Workspace Updates
GenSum
  Changed Additional Description tot Supplemental description
  Changed SUPLEMENTAL INFO TO SPECIAL INSTRUCTIONS
  Fixed problem during create gensum process that was showing sheet numbers as dates
  Updated custom sort to allow items in alternative headings to group
    Example: Roadway alternative heading for item 202E01000
      forced sorting RA202,
      forced sorting to 2nd alternative RA2202
      forced sorting to 3rd alternative RA3202

## Slide 86: Workspace Updates
GenSum Cont.
  Updated to highlight yellow if supplemental desc. Is optional and red if its required. Previously it only highlighted yellow
  The Special Instructions now are prefixed with (Required)and (Optional) for if a supplemental desc is required/optional for an item
OHDOT_Sheets.cell
  Corrected title sheet specification note to match 1302.12.2

## Slide 87: Workspace Updates
OHDOT_GUI.dgnlib/Applications.dgnlib
  Moved named expressions and some ribbon customizations from OHDOT_GUI to Applications.dgnlib for consistency.
  Updated Transoft workflow to with Auto-TURN 2024 and Torus 2025
  Updated workflow visibility to not show Transoft if no Transoft software is installed
OHDOT_v2_WorkSpace.cfg
  Updated loading logic to check registry for 3rd party apps (torus, auto-turn, autotable).
  Also updated loading 3rd party configs from install locations rather than needing to copy 3rd party config files to ORD install locations.

## Slide 88: Workspace Updates
OHDOT_Text_dimension_Styles.dgnlib
  Updated to ORD 2024 Schema
  Added new “title” text styles and text favorites for column style XS Annotations
  Added text favorite for Parcel Name

## Slide 89: Workspace Updates
OHDOT_Features DrainageAndUtilities.dgnlib
  All element templates have color/linestyle/weight defined (fixes some display problems)
  Set default element template for all point feature symbologies (fixed properties dialog showing incorrect symbology for node features)
  Separated Land use FD to use their own feature symbology and element templates to put them on different levels from catchments
  Updated compact database from every 10 opens to 50.

## Slide 90: Workspace Updates
OHDOT_Feature Definitions.dgnlib
  Updated to ORD 2024
  Added new levels and linestlyes for…
    Underground Utility Quality Levels
    Cultivated field/crop limits
    DR_X_LandUse
    SN_P_Post, SN_X_Post
  Added FD for 2-Post Sign Back to back
  Created feature definitions for new utility quality levels
  Several updates for Column Style earthwork XS sheet

## Slide 91: Workspace Updates
OHDOT_Symbols.cel
  Updated signpost cells to match new SN_P_Post and SN_X_Post levels
  Created SG_PMTS_X and SG_PMTS_P cells (pole mounted traffic sensor)
OHDOT_Labels.cel
  Removed from workspace. No longer needed due to place label command being reverted back to microstation version.
OHDOT_Sheets.cel
  Added new cells for XS Quantity End Area and Volume
  Copied XS Quantity Table from OHDOT_Labels.cel
OHDOT_Drainage.cel
  Scaled drainage flow arow cells for better legibility and consistent size

## Slide 92: Workspace Updates
OHDOT_Tempalates.itl
  Created Single Slope 81” barrier component
  Created 301-8E asphalt and jointed concrete pavement shoulder commponents
Survey Master
  Major update released!
OCCS_OSIP_WMS
  All files corrected for new OGRIP Service
  Added .xsw sister files for each county

## Slide 93: Workspace Updates
OHDOT_SheetSeeds_SurvFt.dgnlib
  Updated to ORD 2024
  Added/Modified Cross Section Drawing seeds for column style earthwork XS sheet.
  Renamed Cross Section X-Scale to Cross Section X-Scale (OLD EW Table)
Crash-DRAW Compatibility Fix
  ORD 2024 fixes Crash-DRAW crashing issue on certain types of laptops/devices.

## Slide 94: Cross section SHEET Earthwork Format
Matt Eiben, ODOT CADD & Mapping Services

## Slide 95: Cross section Earthwork Format
July 2025 updates to L&D 3*, Sample Plans, & workspace included revisions to restore the XS sheet earthwork/seeding column format on the left/right edges of sheet as was historically produced for 100+ years.
*L&D 3 verbiage for 1310.3.1 Earthwork Calculations & 1310.3.4 Seeding Calculations was never changed to reflect “table” format, so these changes align with L&D again.

## Slide 96: “table” format example

## Slide 97: “column” format example

## Slide 98: Why?
Bentley’s ORD earthwork table example was difficult to work with especially when:
  Including additional areas/volumes for Roads for Maintaining Traffic, Item 204, geotextile fabric, etc…
  Adding or deducting for drives or intersections between sections.
  Adding match lines; too troublesome, they get in the way and take up space for linework and annotations.

## Slide 99: Sample plan example – previous cadd standards

## Slide 100: Sample plan example – present cadd standards

## Slide 101: What did we do?
Reformatted/New Drawing Seeds.
Reformatted/New Annotation Groups.
Created new cells for cut & fill end areas & volumes.

## Slide 102: What did we do?
Renamed “table” format Drawing Seeds to begin with ~ (tilde) & include “(OLD EW TABLE)” in the names.
Renamed “table” format Annotation Groups to begin “z” & include “(OLD EW TABLE)” in the names.
New “column” format Drawing Seeds & Annotation Groups use same names as previously used.

## Slide 103: What did we do?
Moved offset and datum elevation labels inside grid for better white space management.
First section now aligns with bottom sheet border.
Decreased spacing between sections to attempt fit more sections on a sheet.
  This was configuration variable change so applies to both formats.
  See Ideas Slide and vote for top grid fix.

## Slide 104: What did we do?
Named Boundary offset values changed from table format.
Named Boundary Left Offset values -XX.999999 are intentional; it stops the left offset labels at border edge from overlapping with the datum elevation label.
Removed the PGL/XGL prefixes.

## Slide 105: What did we do?
Added a Minor Grid Annotation Definition to the Annotation Groups.
  However, it’s not enabled by default.
  To enable change Minor Grid Line Properties for Horizontal & Vertical Grid “Full Line.”
  Use is optional.
  Some users have requested this functionality.

## Slide 106: Old “table” format example

## Slide 107: New again “column” format example

## Slide 108: When to implement on projects?
When should we implement on projects already in production?
  If XS sheets were already cut, continue with table format. Annotation Groups already copied in your XS .dgn.
  Project has 50% of the XS created with table format, use seed for the “(OLD EW TABLE)” formatting so they match and you’re not recreating XS sheets.
  Potential challenge: if need to add additional sections within same .dgn.

## Slide 109: Miscellaneous cross Section Defects
End area/volume text justification does not honor center justification; it’s being left justified.
  You couldn’t notice this with the table format.
ORD 2024 - 2.0:1 (vs. 2:1) slope ratio annotations.
  See Q&A #11 - Ohio DOT & Consultants - FAQs & Common/Known Issues of ODOT's Migration to Bentley's OpenX 202
ORD 2024 - Recutting XS sheets using the “Create Cross Section Sheets from Drawings” option, the first section on each sheet is always place far off the sheet.

## Slide 110: Bentley Civil Ideas Portal – cross sections
ORD Seeding Reports Like GEOPAK
End Area Earthwork Corrections for Curvature
Ability to Delete specific Annotation group instance instead of all instances
Ability to annotate models over a station range
Place Cross Section Named Boundary/Create Drawing - round top grid to nearest major interval
Split Cross Sections if Elements in Model Extend Outside of Default Width

## Slide 111: Cross section – reminders!!!
L&D Vol. 3, 1310.2 has not changed due to ORD workflows…

## Slide 112: Cross section – reminders!!!
Sections should look like this:
Not like this:

## Slide 113: Cross section – reminders!!!
Currently, subgrade components are not included in our template/component library.
Add Subgrade Component to Template KB/wiki
https://bentleysystems.service-now.com/community?id=kb_article_view&sysparm_article=KB0024526

## Slide 114: future cross section item
Possible future change
  Look at modification to annotation group to not display pavement cross slopes.
  I have a method that should work but may not be foolproof.
  If you have something that has been working for you, please contact me.

## Slide 115: Networking Break 2
Don’t be this guy

## Slide 116: Level of development / model element breakdown Overview
Matt Eiben, ODOT CADD & Mapping Services

## Slide 117: LOD/MEB Overview
As part of our digital project delivery efforts & BIM Strategy Plan, we needed to develop a framework for Level of Development (LOD) and Model Element Breakdown (MEB).
Michael Baker International prepared: Level Of Development & Model Element Breakdown Report, June 30, 2025.

## Slide 118: WHAT IS LEVEL OF DEVELOPMENT (LOD)?
Also known as Level of Information Need (LOIN) but LOIN has more “info.” attached to model elements.
Communicates the reliability of interpreting model elements at different project stages.
A method for managing risk by transparently conveying confidence and accuracy during the letting process and standardizing modeling practices during design development.

## Slide 119: WHAT IS LEVEL OF DEVELOPMENT (LOD)?
Generally, LOD is represented on a scale of 100 (low) to 500 (high) which provides clarity on the following aspects of model objects:
  Dimensional representation of an object (2D vs. 3D).
  Measurement attributes (size, shape, orientation).
  Reliability of how the model element interfaces with other objects.
  Additional features, such as whether the object has been developed through analysis, provide detail and instructions for fabrication or contain asset information as attributes.

## Slide 120: WHY IS LOD IMPORTANT?
LOD is essential for clarity and consistency in BIM workflows.
It helps project teams articulate the progression of model elements, ensuring that stakeholders understand the usability and limitations of the data they receive.
Without LOD, misinterpretations can lead to costly errors and inefficiencies.

## Slide 121: Aashto & jtcees fundamental lod definitions
AASHTO – American Association of State Highway and Transportation Officials JTCEES – Joint Technical Committee on Electronic Engineer Standards

## Slide 122: Odot base LOD DEFINITIONS

## Slide 123: Odot base LOD DEFINITIONS

## Slide 124: Odot base LOD DEFINITIONS

## Slide 125: Odot base LOD DEFINITIONS

## Slide 126: Odot base LOD DEFINITIONS

## Slide 127: LOD DEFINITION MATRIX

## Slide 128: What is model element Breakdown (meb)?
MEB is the organization of elements within a digital model and their LOD at different submissions, or stages, within the project lifecycle.
It also groups elements into categories and classes which further standardizes BIM implementation.
Through MEB tools, LOD can be communicated to downstream users.

## Slide 129: TEXAS DOT MEB TOOL EXAMPLE

## Slide 130: ODOT MEB TOOL
In addition to the LOD definitions and matrix, ODOT has developed a template MEB spreadsheet.
The MEB is broken into groups corresponding to ODOT’s C&MS:
  CMS 200: Earthwork
  CMS 300: Subgrade Treatments and Base
  CMS 400: Surface Courses and Pavements
  CMS 500: Structures
  CMS 600: Incidentals (Linear Elements, Lighting, Signs, Traffic Signals)
  CMS 640: Pavement Marking
  CMS 650: Roadsides

## Slide 131: ODOT MEB TOOL
The intent for this tool is for design teams to refer to the guidance provided and document the model development to ensure model elements meet target LOD thresholds.
This tool, either fully or in part, is also provided as project-specific documentation to the contractor when model files are included as part of the construction package.

## Slide 132: ODOT MEB TOOL EXAMPLE
CMS 400 - Surface Courses and Pavements |  |  |  |  |  |  |  |  |  | 
Specification Number | Model Element Name | Method of Measurement | Included in Project? | LOD Minimum | 2D/3D | Reference Specification Number(s) | Comments/Notes | Modeling Criteria |  | 
 |  |  |  |  |  |  |  | 60% Submission | 90% Submission | Final Federated Model
401 | Asphalt Concrete Field Operations | NA | No | NA | NA | 440, 702, 705 | Not a pay item. | NA | NA | NA
402 | Asphalt Concrete Mixing Plants | NA | No | NA | NA | - | Not a pay item. | NA | NA | NA
403 | Asphalt Concrete Quality Assurance | NA | No | NA | NA | - | Not a pay item. | NA | NA | NA
407 | Tack Coat | GAL | Yes | 200 | 2D | - | Child of an asphalt layer. Quantity is calculated with an application rate (gallons per square yard) over the entire asphalt layer. | Volume based on preliminary pavement limits and assumed application rate. | Volume based on refined pavement limits and assumed application rate. | Volume based on final pavement limits and assumed application rate.
- | Tack Coat | GAL | Yes | 200 | - | - | - | - | - | -
- | Non-Tracking Tack Coat | GAL | No | 200 | - | - | - | - | - | -
- | Tack Coat, 702.13 | GAL | No | 200 | - | - | - | - | - | -
408 | Prime Coat | GAL | No | 300 | 3D | - | Child of an asphalt layer. Quantity is calculated with an application rate (gallons per square yard) over the entire asphalt layer. | Volume based on preliminary pavement limits and assumed application rate. | Volume based on refined pavement limits and assumed application rate. | Volume based on final pavement limits and assumed application rate.
409 | Sawing and Sealing Asphalt Concrete Pavement Joints | FT | No | 200 | 2D | 705 | - | Linestring for each pavement joint. Length based on preliminary jointing plan. | Linestring for each pavement joint. Length based on refined jointing plan. | Linestring for each pavement joint. Length based on final jointing plan.
410 | Traffic Compacted Surface | CY, TON | No | NA | NA | 703 | Quantity comes from notes and is not included in model. | NA | NA | NA
411 | Stabilized Crushed Aggregate | CY | No | 300 | 3D | - | - | Area based on preliminary pavement limits. Depth based on preliminary pavement design. | Area based on refined pavement limits. Depth based on refined pavement design. | Area based on final pavement limits. Depth based on final pavement design.

## Slide 133: Recommendations & Next steps
Work/Task Groups to review MEB table.
Develop structures MEB table.
Validate LOD definitions and element through pilot projects.
Change Management for LOD implementation and adoption.
Stay tuned, more to come…

## Slide 134: Heep LOIN (Level of Info. Need) and ISO-19650 webinar
https://www.heep.org/sigs

## Slide 135: Plan Quality
Matt Eiben, ODOT CADD & Mapping Services

## Slide 136: Plan quality
Preventable plan quality errors and omissions have been observed at all stages of a project's lifecycle.
ODOT has been in discussions with ACEC about how as an industry we can make our plan quality better.
Contractors have been building more risk into their bids due to plan quality.

## Slide 137: Not just an Odot problem, industry-wide
https://www.linkedin.com/pulse/why-design-drawings-getting-worse-explained-aec-igor-goriatchev-irezf/

## Slide 138: Not just an Odot problem, industry-wide
Loss of Practical Skills & Hands-On Knowledge
Today’s design teams might be sharp on software, but they often lack practical experience in construction, or even basic drafting & plan preparation.
Gone are the days when people used to work their way up, learning the nuts and bolts of construction before moving into design roles.
This shift suggests that drawings may look polished, but they do not consider practical challenges arising on-site.

## Slide 139: Not just an Odot problem, industry-wide
Over-reliance on Automation and BIM Tool
Unwanted side effect has been a lack of critical thinking when it comes to drafting.
Automation can drive technically correct drawings that may miss the big picture.
Drawings often become muddled when using powerful software, and misunderstandings occur in the field. For a long time, competent pros could catch this.

## Slide 140: Not just an Odot problem, industry-wide
Speed vs. Quality
Teams are being pushed to complete more in less time.
When designers and detailers race against time, the quality of drawings suffers.
Modeling on such a rushed timeline may lack review and check details in which mistakes are caught. These mistakes then appear on site when the work actually starts.
Key information that otherwise may have been checked to meet a deadline is skimmed over, leading to costly rework or delays.

## Slide 141: Not just an Odot problem, industry-wide
Remote Work and the Loss of In-Person Mentorship
Changed how we receive training and mentorship.
Online meetings and emails, can’t replicate the same learning experience as face-to-face mentorship.
Junior designers never have the opportunity to acquire the practical knowledge that would have made their drawings accurate. The result is drawings devoid of the depth and cohesion they previously had.

## Slide 142: Not just an Odot problem, industry-wide
Budget Cuts and the Push for “Cheaper, Faster”
When budgets are cut short, quality is mostly sacrificed.
Less time, fewer resources, and much pressure affect drawing quality.
Many say, “You get what you pay for,” as reduced fees result in rushed, incomplete, or inconsistent drawings.
Budget cuts also cut down on the time available for quality control.

## Slide 143: Not just an Odot problem, industry-wide
“Just Get It Done” Mentality
Increasingly leaning toward a “just make it work” perspective, where teams are forced to deliver projects without having nailed down all of the details.
Incomplete drawings being rushed out the door to meet deadlines, followed by endless RFIs from the field.
Instead of thorough, coordinated models, we’re left with drawings that require additional clarification on-site, slowing down progress and adding costs.

## Slide 144: Back to basics - Drafting 101 per l&d 3 Section 1202
How many of you are familiar with L&D 3 Section 1202 Drafting ?
  It’s not the bible of drafting standards but provides great guidance for basics things that are often done poorly.
When was the last time you reviewed it ?
When was the last time you referred a colleague to this section for guidance ?

## Slide 145: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.1 Plan Scales
Prepare plans keeping in mind that a 22”x34” full-size plan sheet may be reproduced to an 11”x17”print.
It is recommended that plan sheet scales normally be limited to the following: 1:1, 1:5, 1:10, 1:20, 1:50, 1:100, 1:200, 1:500 or 1:1000.

## Slide 146: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.2 Lettering
Lettering should be oriented in such a manner that it can be read from either the bottom or right side of the plan sheet.

## Slide 147: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.3 Cross-Section Grids
Letters and lines should be bolder when they are superimposed over cross-section grids.
1202.4 Drafting Conventions
The preferred standard drafting guidelines for roadway construction plans.

## Slide 148: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.1 Text Orientation
Text on inclined lines should be orientated as shown.

## Slide 149: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.2 Placement of Leaders from Notes
Leader lines should originate from the first/top line on the left, the last/bottom line on the right.
The leader should generally be an inclined straight line.
Where space prohibits the use of straight leader lines, curved leaders may be used. Curves should be smooth and simple.

## Slide 150: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.2 Placement of Leaders from Notes

## Slide 151: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.3 Placement of Leaders to, or from, a Circular Object
A leader to, or from, a circular object should extend radially, so that if extended it would pass through the center of the circle.

## Slide 152: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.4 Terminators
Leaders should terminate with an arrowhead when pointing to an object or to an edge.
Should terminate as shown when pointing to a surface or layer.

## Slide 153: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.5 Placement of Balloons
Balloons on typical sections should be aligned as much as possible.
The leader lines extending from the bubbles to pavement layers should be vertical, where possible.
Other items, such as guardrail and underdrains may be labeled with straight, inclined, leaders.
All leaders should end with a terminator.

## Slide 154: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.5 Placement of Balloons

## Slide 155: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.7 Overdrafting
It is preferable to place dimensions outside areas which contain cross-hatching and other line work.
Where not possible, the cross-hatching, or line work, should be broken around the text.
Hatch lines should never cross through text, however, certain critical line work elements, such as centerlines may pass through text.
Masked text doesn’t give you permission to place text over linework!

## Slide 156: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.7 Overdrafting

## Slide 157: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.11 Placement of Dimension Text
Text should be placed above a solid dimension line and oriented parallel to the line.
Horizontal text shall be read parallel to the bottom edge of the sheet.
Vertical text shall be read parallel to the right edge of the sheet.
Text in dimension strings should be placed at the same level.

## Slide 158: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.11 Placement of Dimension Text

## Slide 159: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.11 Placement of Dimension Text

## Slide 160: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.13 Dimensions in Crowded Conditions
In crowded conditions, gaps in extension lines near arrowheads may be left as shown below, in order to clarify the dimensions.

## Slide 161: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.16 Dimensioning an Object
Place shorter dimensions nearest to the object outline.
Crossing extension lines is acceptable.
Dimension lines should not cross extension lines.
Extension lines should not be shortened.
Dimension line should never coincide with or form a continuation of any line of the drawing.
If possible, dimensions should always be placed off the object.

## Slide 162: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.16 Dimensioning an Object

## Slide 163: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.17 Crossing Dimension Lines
Extension lines should not be broken.
Lines should not be centered at object edges.
Crossing extension lines is acceptable.

## Slide 164: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.18 Grouped Dimensions
Grouped dimensions should be in line, evenly spaced and off the object being dimensioned.

## Slide 165: Back to basics - Drafting 101 per l&d 3 Section 1202
1202.4.19 Use of “Typical”
For symmetrical objects and repetitive dimensions, use the word “typical” to simplify dimensioning, as shown:

## Slide 166: Back to basics - Drafting 101

## Slide 167: Thank you