## Slide 1: ODOT Safety committee• December 9, 2021
Notes: Welcome and intro

## Slide 2: Cuy-271-8.36 Safety funding application ODOT District 12
Brian Blayney, ODOT District 12

## Slide 3: Area map
CUY-271-8.36 Funding Presentation
I-71
I-80
SR 82
Cedar
Fairmount
Brainard
Richmond (SR 175)
I-271
10.05
9.75
10.88

## Slide 4: Purpose
Manage queues that extend onto NB I-271 from the Cedar/Brainard exit ramp (Ramp terminal capacity improvement completed on PID 97676 competed in 2018)
Mitigate 161 crashes that occurred within study area on I-271 (2017-2019)
October 19, 2021 7:50 AM

## Slide 5: HSIP Urban Freeway rankings
CUY-271-8.36 Funding Presentation
I-71
I-80
SR 82
2018 UrbFwy, Rank 12
2018 UrbRamp, Rank 98
2018 UrbFwy, Rank 62
2018 UrbFwy, Rank 350
2018 UrbFwy, Rank 458
2020 Urban Freeway Peak Searching Excess Locations (2016-2020), Top 500 |  |  |  |  |  |  | 
Rank | Average Observed Crashes | Predicted Crashes | Expected Crashes | Expected Excess Crashes | NLF ID | Begin Logpoint | End Logpoint
3 | 73.37 | 13.61 | 59.18 | 45.57 | SCUYIR00271**C | 11.072 | 11.172
81 | 34.24 | 13.61 | 29.34 | 15.73 | SCUYIR00271**C | 10.872 | 10.972
187 | 24.15 | 7.97 | 20.65 | 12.68 | SCUYIR00271**C | 9.700 | 9.800
257 | 19.57 | 13.61 | 18.15 | 4.54 | SCUYIR00271**C | 11.272 | 11.372
297 | 17.66 | 13.61 | 16.97 | 3.36 | SCUYIR00271**C | 10.460 | 10.560
433 | 14.45 | 13.61 | 14.31 | 0.70 | SCUYIR00271**C | 10.560 | 10.660

## Slide 6: Existing conditions – Ramp volumes
The right lane on NB I-271 is over capacity – 750 veh to Brainard and 1400 veh to WB Cedar (PM peak)
Traffic entering NB I-271 from express lanes must cross 3 lanes to exit
AM and PM exiting DHV’s are nearly identical

## Slide 7: ExISTING CONDITIONS - CRASHES
296 crashes occurred NB I-271 between log points 8.36 to 11.40 including interchange ramps (2017 to 2019)
Rear-end and sideswipe-passing crashes comprise 82 percent of all crashes.
2018 HSIP Urban Freeway segments #12, #62, #350, and #452.

## Slide 8: Examples of diagrams from OH1 Narratives…
Notes: 10/8/2019

## Slide 9: countermeasures
Reverse express lane entrance and exit access with I-271 local lanes between Chagrin and Cedar, adding another 3000’ to provide more room for weaving
Existing Condition
Proposed Condition

## Slide 10: Countermeasures
Convert exit diverge from one lane to two lanes to uncork bottleneck to the Cedar loop ramp, providing a second lane to store traffic
Extend deceleration lane for Cedar/Brainard exit ramp 1600’ further south to provide storage for queued traffic when Brainard and Cedar exits are slammed

## Slide 11: Design challenges, proposed improvements

## Slide 12: Aux lane addition under fairmount w/ shift
65’ opening under Fairmount
Four 12’ lanes fit, 10’ outer shoulder
A 7’ wide inside shoulder is recommended for a short distance, DE required
65’

## Slide 13: Two-lane diverge under cedar overpass
78’ opening under Cedar
Shift 5’ to median
Five 12’ lanes, 10’ inside shoulder
An 8’ wide outside
No DE required for ramp shoulder
78’

## Slide 14: Avoid recently installed noise barrier ☹
Deceleration lane begins at ½ MILE sign
Shift 10’ to median to maintain clearance to guardrail for noise barrier
No DE required for ramp shoulder

## Slide 15: Coordination with other projects…
Desired to be combined with upcoming PM overlay on I-271 local lanes (PID 104380, FY2025) to reduce cost of Safety request (for surface course, markings)
Plans will be prepared on Part 1/Part 2 format, just in case they need to be split and sold separately
D12 is requesting design services in January 2022 Programmatic to ensure plans are ready for implementation

## Slide 16: Cost summary
$3.890 M Construction Cost
Eng Design ~ $704,000
  D12 will fund PE and DD design phases
  $82,000 already spent on development, refinement
Additional R/W not required

## Slide 17: B/C Ratio
Safety Ask Based on Safety Benefits Estimated in ECAT to produce a B/C ratio approximately 1.0
  “Lengthen Ramp” CMF1 = 0.80
  “Extend the Left/Right Turn Lane” (VDOT) CMF2 = 0.85
  “Lengthen Weave Distance” CMF3 = 0.70 (only applied between 10.05 to 10.92)
Notes: -Lengthen Ramp CMF applied to 37 crashes on the exit ramp, all crashes
-Extend Turn Lane CMF applied to 29 crashes at the Brainard intersection
-Lengthen Weave CMF applied to 95 crashes on I-271 local lanes, only to rear-end’s and sideswipes

## Slide 18: Questions
?
Last updated 12/8/2021